## Slide 1
Research of CB ECRIS plasma with the aid of injected 1+ beam
H Koivisto1, O Tarvainen1, T Lamy2, J Angot2, T Thuillier2, P Delahaye3, L Maunoury3, J Choinski4, L Standylo4, A Galatà5, G Patti5
1 University of Jyväskylä, Department of Physics, 40500 Jyväskylä, Finland
2 LPSC, Université Grenoble-Alpes, CNRS/IN2P3, 53 Rue des Martyrs, 38026 Grenoble Cedex, France
3 GANIL, CEA/DSM-CNRS/IN2P3, Caen Cedex 05, France
4 Heavy Ion Laboratory, University of Warsaw, 00-927 Warszawa, Poland
5 INFN-Laboratori Nazionali di Legnaro, 35020 Legnaro PD, Italy
Emilie collaboration

## Slide 2
Global efficiency measurements with LPSC CB ECRIS
An anomalous global efficiency of the extracted 1+ beam was discovered at the LPSC charge breeder.
Different characteristics for neutral and 1+ beam injection
It was assumed and later confirmed that a fraction of injected 1+ beam propagates through the charge breeder plasma (oxygen) without being captured and ionized.
Can we use this as a diagnostic tool?
What happens?
Krypton ion beam intensities measured after CB
Koivisto H et al 2014 Rev. Sci. Instrum. 85 02B917

## Slide 3
Experimental setup of LPSC 14.5 GHz PHOENIX CB-ECRIS
to study the properties of 1+ beam
Was used, for example, to define the breeding time

## Slide 4
Similar anomalous 1+ behavior was confirmed with the solid elements
Similar behavior of injected 1+ beam with solid elements
The result indicates that anomalous effect can be connected to plasma processes (not to wall effect). Fraction of 1+ beam propagates through the plasma without capture and ionization process
Rb
Cs
Assumption: In-flight ionized
Assumption: these ions propagate through CB “without” interacting with plasma

## Slide 5
Figure: Normalized intensities of various charge states of rubidium (85Rb) and cesium(133Cs) ions, measured after the mass separation of CB, as a function of DV.
Note the drastically different behavior of 1+ and 2+ ions when compared to high charge states.
Normalised production efficiency as a function of DV
“Beam components”
“Plasma components”

## Slide 6
Figure: Breeding times of low and high charge state 133Cs ions.
Note: Behavior of 1+ and 2 plasma are practically identical with and without the plasma
Indicates that fraction of 1+ and 2+ beams propagates through the plasma without any processes affecting the time the ion stays inside the charge breeder.
“Breeding” time: low vs high charge states
Captured 1+ ions strongly
modify the plasma!

## Slide 7
Theoretical explanation for efficiency vs DV behavior
Slowing down coefficient in ion-ion collisions (can be associated with beam “component” to plasma “component” transition, i.e to capture efficiency )
where
with
R(uab) reaches a maximum when longitudinal component of the incident ion velocity,
va,∥, equals the average velocity of the plasma ions 〈vb 〉.
Note strong charge state dependence!
and a refer to 1+ component

## Slide 8
Experimentally recorded, normalized charge breeding efficiency of Rb20+ together with normalized R(uab)- factor
Experimental data versus theoretical curve
By DV tuning we are maximizing the slowing down coefficient!
O Tarvainen et. al., Plasma Sources Sci. Technol. 24 (2015) 035014

## Slide 9
Concept of reaction cross section s and mean free path l
A particle having a “diameter” of z suffers a reaction with another particle if anywhere its center is within distance z of the center of another particle. Therefore it sweeps out, without collision, a cylinder of diameter 2z. We obtain that the cross section for the reaction is:
v
2z
The volume V of the cylinder is:
L=vt
The number of reactions the particle
experiences during the path L is:
Velocity of particle (1+ beam)
(nparticles = density of target particles)
Distance between the subsequent reactions, i.e. mean free path l is:
s [m2]: any cross section
n [1/m3]: density of any targets
Note: In this case the target particle is not moving. If projectile and target atoms have same velocities the equation has to be divided by 21/2

## Slide 10
Concept of reaction cross section s and mean free path l
The probability P for (any) reaction is:
The intensity I decreases as:
By the integration we obtain:
=1/l
Lets find out how the 1+ intensity decreases when it propagates through the plasma
This gives the decay of intensity due to (intensity decreasing) reactions inside the CB. Can be used to find out the mean free path…
(slow background, “fast” beam)
II/10
Intensity has dropped to 1/e (from it’s original value) when beam has propagated the distance of x = l

## Slide 11
Mean free path lc for collisional capture (for 1+ beam)
where li is mean free path for in-flight ionization and L effective plasma length
Transported 1+ intensity with and without plasma
Using the experimental data (behavior of injected 1+ beam intensity), and frequency scaling of collisions ( ) we can calculate the mean free path (upper limit because we assume single collision) for ion-ion collisions, collision frequency and minimum electron density.
(from optimum slowing down coefficient)
Injected 1+ beam is mainly disturbed by two processes: 1) ion-ion collisions and 2) electron impact ionizations (in-flight). Lets “forgot” ionization at this point (for simplicity)

## Slide 12
Ion-ion collision mean free path for 1+ beam (≈ intensity dropped to value of 36 %)
Ion-ion collision frequency (minimum)
Transition charge state (magnetized -> non-magnetized)
Minimum plasma density
Parameters obtained from 1+ vs deltaV behavior
[mm]
[mm]
[MHz]
[MHz]
[1/cm3]

## Slide 13
Mean free path and (minimum) collision frequency as a function of charge state
For more information see: O Tarvainen et. al., Plasma Sources Sci. Technol. 24 (2015) 035014

## Slide 14
The effect of ionizing collisions on the estimated plasma parameters.
s: ionization cross section
ve: electron velocity
vi: injected 1+ velocity (optimized velocity)
Estimated in-flight correction factor:
: rate coefficient
O Tarvainen et. al., Plasma Sources Sci. Technol. 24 (2015) 035014

## Slide 15
Maximum electron density
Earlier we got minimum electron density of plasma. How to get the upper limit?
Lets make an assumption: we must first ionize the 1+ ion to charge state 2+ in order to increase the capture probability. Now we can define the electron density because we know:
Mean free path from the experiments
Optimal ion velocity from slowing factor equation (DV has been optimized)
Ionization rate coefficient
As a result the upper limit for electron density shows below can be calculated

## Slide 16
Injection efficiency of lighter 1+ beam and lighter mixing gas element (main plasma component)
Power [W] | 150 | 250 | 350 | 470
lRb1+ | 132 | 84 | 62 | 48
nii, Rb1+ | 14 | 22 | 30 | 38
Ne: 1.6 . 1011 to 4.4 . 1011
Na1+ injected into He plasma (6 eV)
Rb1+ injected into O plasma (8 eV)
Ne: 1.2 . 1011 to 3.2 . 1011
Comparison to Rb injection:
O. Tarvainen et. al., accepted for publication in Phys. Rev. Acceler. and Beams

## Slide 17
Measured and simulated Na1+ transport efficiency as a function of DV
Global efficiencies:
Na in He: 20-30 %
Rb in O: 50-60 %
Possible explanation for lower capture efficiency:
Lower average charge state of He plasma.
Pµ: 470 W
Simulations by A. Galata
O. Tarvainen et. al., accepted for publication in Phys. Rev. Acceler. and Beams

## Slide 18
Measured and simulated Na1+ transport efficiency as a function of DV
Good agreement between simulations and experimental data

## Slide 19
Beam currents of the buffer gas species are affected by the 1+ injection
The magnitude of the effect follows the injected current linearly
This is probably due to gas mixing effect which is believed to affect the confinement times of both the heavier and lighter species
Effect of injected heavier element on the intensity of the mixing gas element

## Slide 20
Can we use 1+ injection and charge breeding to study the gas mixing effect on ion confinement times?
Question for future experiments

## Slide 21
Particle balance equation for charge state q
Loss term defined by ion confinement time
How to measure the confinement time with the 1+ injection method?
Switch on the 1+ injection (preferable alkali metal)
Wait until high charge state currents have been saturated
Switch off the 1+ injection
Measure the decay constant immediately following the trailing edge of the 1+ pulse.
Obtain ion confinement time.

## Slide 22
If the procedure is repeated with different buffer gas / injected ion species combinations, the effect of gas mixing on the ion confinement time can be measured at least qualitatively.
First direct measurement of the effect!
Can be performed also with a conventional ECRIS using a pulsed sputter sample and the results can be compared to separate the gas mixing effect on the capture and confinement.